## Slide 1
Implementation in SGrPython
OpenCEM
REST API
Device B
SERIAL
Device C
MODBUS Device A
Automatic generation of External Interfaces from XSD schemes (prepared by SGrPython for each transport type)
Each device in OpenCEM is connected to an External Interface through a «SmartGridReady Component» Object
Prof. Dr. D. Zogg, Sept 2022
XML
A
XML
B
XML
C
XML: External Interface Description
External Interfaces
ei_modbus
ei_rest_api
ei_serial
XSD
MODBUS
XSD
REST API
Schemes
XSD
SERIAL
SmartGridReady Component
Objects
Device Objects (Heat Pump,
EV Charger, Boiler, etc.)
Device A
Device B
Device C
SGr A
SGr B
SGr C
Reading in of XML files for each supported device at startup